## Slide 1: Advanced Computer Networks
  Packet Switching vs. Circuit Switching

## Slide 2: A Simple Switching Network
Station
Node

## Slide 3: Data Networks
Communication by transmitting data through a network of intermediate switching nodes
Switching nodes not concerned with content
End devices referred to as stations
  Computers, terminals, telephones, etc.
Nodes connected by transmission links (trunks), in some topology.
Station attaches to node (by access links)
Collection of nodes is a communications network

## Slide 4: Circuit Switching
Dedicated path between two stations
  Connected sequence of links between nodes
  E.g telephone network
Communication involves three phases
  Circuit establishment
  Data transfer
  Circuit disconnect

## Slide 5: Circuit Establishment
Station A to node 4 requesting connection to station E
Circuit from A to 4 usually dedicated line
Node 4 finds next leg to node 6
Based on routing information, availability, cost, node 4 selects circuit to node 5
Allocates a free channel
  TDM [time-division multiplexing]
  FDM [frequency-division multiplexing]
Node 4 requests connection to E
And so on
What is Multiplexing ?

## Slide 6: Data Transfer
Data may be digital (e.g., terminal to host) or analog (e.g., voice)
Signaling and transmission may each be digital or analog
Path is A-4 circuit, internal switching through 4, 4-5 channel, internal switching through 5, 5-6 channel, internal switching through 6, 6-E circuit
Generally, full duplex (data in both directions)
Data , Signaling, Transmission

## Slide 7: Circuit Disconnect
Connection terminated
  Usually by one of the stations
Signals to 4, 5, and 6 to de-allocate resources

## Slide 8: Circuit Switching - Notes
Connection established before data transmission begins
Channel capacity must be available and reserved.
Nodes must have capacity to handle connection
Switches must have intelligence to make allocations and devise route

## Slide 9: Circuit Switching - Notes
Can be inefficient
  Capacity dedicated for duration of connection
    Even if no data are being transferred
  For voice, utilization high, but still doesn’t approach 100%
  For terminal connection, may be idle most of the time
  Delay prior to data transfer for call establishment
  Once circuit established, network transparent to users
  Data transmitted at fixed rate
    No delay other than propagation
    Delay at node negligible

## Slide 10: Packet Switching – Circuit Switching Issues
Designed for voice
Resources dedicated to particular call
For voice, high utilization
  Most of the time, someone is talking
For data
  Line idle much of the time
  Constant data rate
    Limits interconnection of variety of host computers and terminals

## Slide 11: Packet Switching – Basic Operation
Data are transmitted in short blocks, called packets, typical upper bound 1000 octets (bytes)
Longer messages broken up into series of packets
Transmitting computer sends message as sequence of packets.
Packet includes control information including destination station.
Packets sent to node to which sending station attaches
Node stores packet briefly, determines next leg of route, and queues packet to go out on that link
When link is available, packet is transmitted to next node
All packets eventually work their way through network

## Slide 12: The Use of Packets

## Slide 13: Packet Switching – Advantages
Line efficiency greater
  Node-to-node link dynamically shared by many packets
Data-rate conversion
  Each station connects to its node at its proper data rate
  Nodes act as buffers
Packets accepted, even under heavy traffic, but delivery delay increases
  Circuit switching networks would block new connections
Priorities can be used

## Slide 14: Packet Switching – Disadvantages
Delay
  Transmission delay equal to length of packet divided by incoming channel rate
  Variable delay due to processing and queuing
Packets may vary in length, take different routes, …
  May be subject to varying delays
  Overall packet delay can vary substantially (jitter)
  Not good for real-time applications like voice and real-time video
Overheads including address of destination, sequencing information added to packet
  Reduces capacity available for user data
More processing required at node

## Slide 15: Packet Switching Techniques
Datagram
  Each packet is treated independently.
Virtual Circuit
  Sending packets via a preplanned route, similar to circuit switching.

## Slide 16: Switching Technique - Datagram
Datagram: each packet treated independently
  No reference to packets that have gone before
  Each node chooses next node on path
  Packets with same destination address do not follow same route
  May arrive out of sequence
  Exit node or destination restores packets to original order
  Packet may be destroyed in transit
  Either exit node or destination detects loss and recovers
Call setup avoided
For an exchange of a few packets, datagram quicker
More flexible.
  E.g. Routing away from the congestion
  Delivery is inherently more reliable
    If a node fails, subsequent packets may be re-routed

## Slide 17: Packet Switching: Datagram Approach

## Slide 18: Packet Switching Technique – Virtual Circuit
Preplanned route established before packets sent
All packets follow same route
Similar to circuit in circuit-switching network
  Hence virtual circuit
Each packet has virtual circuit identifier
  Nodes on route know where to direct packets
  No routing decisions
Not dedicated path, as in circuit switching
  Packet still buffered at node and queued for output
  Routing decision made once for that virtual circuit
Network may provide services related to virtual circuit
  Sequencing and error control
Packets should transit more rapidly
If node fails, all virtual circuits through node lost

## Slide 19: Packet Switching: Virtual-Circuit Approach

## Slide 20: Discussion
Data comm. Vs. Voice comm.
What if the Internet is circuit-switching?
What if the telephone network is packet-switching?
The failure of WAP (Wireless Application Protocol)
Internet Telephony vs. PSTN
PSTN: Public Switching Telephone Network