## Slide 1: OSI vs. TCP/IP
想像一下，你是彗星撞地球後的倖存者，
這個世界正待你來重建，你是網路專家，
如果要重新打造一個Internet…

## Slide 2
開啟電腦(筆電)，自動連上(無線)網路後，開啟Web Browser， 輸入https://www.im.ncnu.edu.tw/
Which protocols are used?
2. Which network devices/servers are required?

## Slide 3
ChatGPT

## Slide 4
ChatGPT

## Slide 5: Need For Protocol Architecture
File transfer as an example
  Source must activate communication path or inform network of destination
  Source must check destination is prepared to receive
  File transfer application on source must check destination file management system will accept and store file for his user
  May need file format translation
Task broken into subtasks
Implemented separately in layers in stack
Functions needed in both systems
Peer layers communicate

## Slide 6: Key Elements of a Protocol
The peer layers communicates by means of formatted blocks of data that obey a set of rules and conventions known as a protocol.
Key elements:
  Syntax
    Format of the data blocks
    Signal levels
  Semantics
    Control information for coordination and error handling
  Timing
    Speed matching
    Sequencing

## Slide 7: Protocol Architecture
Task of communication broken up into modules
For example, file transfer could use three modules:
  File transfer application
  Communication service module
  Network access module

## Slide 8: Simplified Architecture for File Transfer

## Slide 9: Protocol Architectures and Networks

## Slide 10: Addressing Requirements
Two levels of addressing required
Each computer needs unique network address
Each application on a (multi-tasking) computer needs a unique address within the computer
  The service access point or SAP
  The port on TCP/IP stacks

## Slide 11: Protocols in Simplified Architecture

## Slide 12: Protocol Data Units (PDU)
At each layer, protocols are used to communicate
Control information is added to user data at each layer (PDU = Control + Data)
Transport layer may fragment user data
Each fragment has a transport header added
  Destination SAP (port)
  Sequence number
  Error detection code
This gives a transport protocol data unit

## Slide 13: Protocol Data Units, PDUs

## Slide 14: Operation of a Protocol Architecture

## Slide 15: Standardized Protocol Architectures
Required for devices to communicate
Vendors have more marketable products
Customers can insist on standards based equipment
Two standards:
  OSI Reference model
    Never lived up to early promises
  TCP/IP protocol suite
    Most widely used

## Slide 16: OSI
Open Systems Interconnection
Developed by the International Organization for Standardization (ISO)
Seven layers
A theoretical system delivered too late!
TCP/IP is the de facto standard

## Slide 17: OSI - The Model
A layer model
Each layer performs a subset of the required communication functions
Each layer relies on the next lower layer to perform more primitive functions
Each layer provides services to the next higher layer
Changes in one layer should not require changes in other layers

## Slide 18: OSI Seven Layers

## Slide 19: The OSI Environment

## Slide 20: OSI as Framework for Standardization
Service
Protocol

## Slide 21: Layer Specific Standards
1
3
2

## Slide 22: Elements of Standardization
Protocol specification
  Operates between the same layer on two systems
  May involve different operating system
  Protocol specification must be precise
    Format of data units
    Semantics of all fields
    allowable sequence of PDUs
Service definition
  Functional description of what is provided
Addressing
  Referenced by SAPs

## Slide 23: Service Primitives and Parameters
Services between adjacent layers expressed in terms of primitives and parameters
Primitives specify function to be performed
Parameters pass data and control info

## Slide 24: Primitive Types
REQUEST | A primitive issued by a service user to invoke some service and to pass the parameters needed to specify fully the requested service
INDICATION | A primitive issued by a service provider either to: indicate that a procedure has been invoked by the peer service user on the connection and to provide the associated parameters, or notify the service user of a provider-initiated action
RESPONSE | A primitive issued by a service user to acknowledge or complete some procedure previously invoked by an indication to that user
CONFIRM | A primitive issued by a service provider to acknowledge or complete some procedure previously invoked by a request by the service user

## Slide 25: Service Primitive Types
Layer N
Layer N
Request
Indication
Response
Confirm

## Slide 26: Timing Sequence for Service Primitives

## Slide 27: TCP/IP Protocol Architecture
Developed by the US Defense Advanced Research Project Agency (DARPA) for its packet switched network (ARPANET)
Used by the global Internet
No official model but a working one.
      Application layer
      Transport layer
      Internet layer
      Data Link layer
      Physical layer
(host-to-host)
(Network Access Layer)

## Slide 28: Physical Layer
Physical interface between data transmission device (e.g. computer) and transmission medium or network
Characteristics of transmission medium
Signal levels
Data rates
etc.

## Slide 29: Network Access Layer
Exchange of data between end system and network
Destination address provision
Invoking services like priority
Internet Layer (IP)
Systems may be attached to different networks
Routing functions across multiple networks
Implemented in end systems and routers

## Slide 30: Transport Layer (TCP)
Reliable delivery of data
Ordering of delivery
Application Layer
Support for user applications
e.g. HTTP, SMTP

## Slide 31: OSI v TCP/IP
Internet
Standards
IEEE
ISO
ITU-T

## Slide 32: Some Protocols in TCP/IP Suite

## Slide 33: TCP
Usual transport layer is Transmission Control Protocol
  Reliable connection
Connection
  Temporary logical association between entities in different systems
TCP PDU
  Called TCP segment
  Includes source and destination port (c.f. SAP)
    Identify respective users (applications)
    Connection refers to pair of ports
TCP tracks segments between entities on each connection

## Slide 34: UDP
Alternative to TCP is User Datagram Protocol
Not guaranteed delivery
No preservation of sequence
No protection against duplication
Minimum overhead
Adds port addressing to IP

## Slide 35: IP and IPv6
IP (v4) header
  minimum 20 octets (160 bits)
  32-bit source and destination addresses
  Checksum applies to header to avoid incorrect delivery
  Protocol field shows if TCP, UDP etc. carried
  Flags and fragmentation offset used in fragmentation
IPv6
  1995 IPng became standard IPv6 in 1996
  Enhancements for modern high speed networks
  Carry multimedia data streams
  Increase address space (128 bits)

## Slide 36: TCP/IP Concepts

## Slide 37: Addressing level
Level in architecture at which entity is named
Unique address for each end system (computer) and router
Network level address
  IP or internet address (TCP/IP)
  Network service access point or NSAP (OSI)
Process within the system
  Port number (TCP/IP)
  Service access point or SAP (OSI)

## Slide 38: PDUs in TCP/IP

## Slide 39
TCP Header + Telnet Data
Telnet Data

## Slide 40
IP Header + TCP Header + Telnet Data
Ethernet Frame Header + IP Header + TCP Header + Telnet Data

## Slide 41: Example Header Information
Destination port
Sequence number
Checksum

## Slide 42: Internetworking
Most networks not isolated
  Different types of LAN
  Multiple similar LANs
  Multiple sites connected by WAN(s)
May appear as large network
Entire configuration referred to as an internet
Each constituent network is a subnetwork

## Slide 43: Internetworking Devices
Each subnetwork supports communication among devices attached to that subnetwork
  End systems (ESs)
Subnetworks connected by intermediate systems (ISs)
  Provide communications path and relay and routing functions
  Bridges and routers
  Different types of protocols used
Bridge operates at layer 2
  Relay between like networks
Router operates at layer 3
Routes packets between potentially different networks

## Slide 44: Routers
Interconnect dissimilar subnetworks
  Provide a link between networks
  Provide for routing and delivery of data between processes on end systems attached to different networks
  Do not require modifications of architecture of subnetworks
Must accommodate differences among networks
  Addressing schemes
  Maximum packet sizes
  Interfaces
  Reliability
Satisfied by internetworking protocol implemented in all end systems and routers
  IP

## Slide 45: Configuration for TCP/IP Example
ATM: Asynchronous Transfer Mode

## Slide 46: Action of Sender

## Slide 49: Action of Router

## Slide 50: Action of Receiver

## Slide 53: Internetworking Terminology
End System (ES)
  Device attached to one of the networks of an internet
  Supports end-user applications or services
Intermediate System (IS)
  Device used to connect two networks
  Permits communication between ES attached to different networks
Bridge
  IS used to connect two LANs that use similar protocols
  Address filter
  Does not modify packets
  Layer 2 of the OSI model
Router
  IS used to connect two networks that may or may not be similar
  Uses an internet protocol present in each router and each end system of the network
  Layer 3 of the OSI model
"Switch" can be regarded as a multiport bridge.