## Slide 1: Internet Protocols
IPv4 and IPv6

## Slide 2: What is Internet Protocol (IP)?
Protocol for internetworking
IP provides a connectionless, or datagram, service between end systems.
Advantages from IP’s connectionless internet services:
  Flexible: IP can deal with a variety of networks. IP requires little from the constituent networks.
  Robust: IP uses datagram services.
  Best for connectionless transport protocols: No unnecessary overhead

## Slide 3: Internet Protocol Operation
* A  B
Router X makes a decision:
B is in one of the networks to which X is attached.  send
B is in a remote network. Additional routers must be traversed.  routing
X does not know the destination address.
 Error message

## Slide 4: Connectionless Internetworking
Unreliable
  Not guaranteed delivery
  Not guaranteed order of delivery
    Packets can take different routes
  Reliability is responsibility of next layer up (e.g. TCP)

## Slide 5: Design Issues
Routing
Datagram lifetime
Fragmentation and re-assembly
Error control
Flow control

## Slide 6: Routing
End systems and routers maintain routing tables
  Indicate next router to which datagram should be sent
  Static
    May contain alternative routes
  Dynamic
    Flexible response to congestion and errors
Source routing
  Source specifies route as sequential list of routers to be followed
  Security
  Priority
Route recording

## Slide 11: Datagram Lifetime
Datagrams could loop indefinitely
  Consumes resources
  Transport protocol may need upper bound on datagram life
Datagram marked with lifetime
  Time To Live field in IP
  Once lifetime expires, datagram discarded (not forwarded)
  Hop count
    Decrement time to live on passing through a each router
  Time count
    Need to know how long since last router

## Slide 14: Fragmentation and Re-assembly
Different packet sizes
When to re-assemble
  At destination
    Results in packets getting smaller as data traverses internet
  Intermediate re-assembly
    Need large buffers at routers
    Buffers may fill with fragments
    All fragments must go through same router
      Inhibits dynamic routing

## Slide 15: IP Fragmentation
IP re-assembles at destination only
Uses fields in header
  Data Unit Identifier (ID)
    Identifies end system originated datagram
      Source and destination address
      Protocol layer generating data (e.g. TCP)
      Identification supplied by that layer
  Data length
    Length of user data in octets
  Offset
    Position of fragment of user data in original datagram
    In multiples of 64 bits (8 octets)
  More flag
    Indicates that this is not the last fragment

## Slide 16: Fragmentation Example

## Slide 22: Addressing
Addressing level
Addressing scope
Connection identifiers
Addressing mode

## Slide 23: TCP/IP Concepts

## Slide 24: Addressing Level
Level in comms architecture at which entity is named
Unique address for each end system
  e.g. workstation or server
And each intermediate system
  (e.g., router)
Network-level address
  IP address or internet address
  OSI - network service access point (NSAP)
  Used to route PDU through network
At destination data must routed to some process
  Each process assigned an identifier
  TCP/IP port
  Service access point (SAP) in OSI

## Slide 25: Addressing Scope
Global address
  Global nonambiguity
  Global applicability: Any system identifies any other system by means of global address.
  Enables internet to route data between any two systems
Need unique address for each device interface on network
  MAC address on IEEE 802 network and ATM host address
  Enables network to route data units through network and deliver to intended system
  Network attachment point address

## Slide 26: IPv4/v6 Addressing Modes
Unicast
Anycast (in IPv6)
Multicast
Broadcast
Note:
In practice, Multicast/Broadcast packets will not be forwarded by routers.
 Scope of Multicast/Broadcast is limited within a single network.

## Slide 27
Broadcast

## Slide 28
Multicast
23 low order bits
01:00:5e:X’:Y:Z
0xxxxxxx.xxxxxxxx.xxxxxxxx
IP Multicast address: W.X.Y.Z
X’ Y Z

## Slide 29: Internet Protocol (IP) Version 4
Part of TCP/IP
  Used by the Internet
Specifies interface with higher layer
  e.g. TCP
Specifies protocol format and mechanisms
RFC 791
  www.rfc-editor.org
Will (eventually) be replaced by IPv6 (see later)

## Slide 30: IP Services
Primitives
  Functions to be performed
  Form of primitive implementation dependent
    e.g. subroutine call
  Send
    Request transmission of data unit
  Deliver
    Notify user of arrival of data unit
Parameters
  Used to pass data and control info

## Slide 31: Parameters (1)
Source address
Destination address
Protocol
  Recipient e.g. TCP
Type of Service
  Specify treatment of data unit during transmission through networks
Identification
  Source, destination address and user protocol
  Uniquely identifies PDU
  Needed for re-assembly and error reporting
  Send only

## Slide 32: Parameters (2)
Don’t fragment indicator
  Can IP fragment data
  If not, may not be possible to deliver
  Send only
Time to live
  Send only
Data length
Option data
User data

## Slide 33: Options
Security
Source routing (Strict, Loose)
Route recording
Stream identification
Timestamp

## Slide 34
Milliseconds since midnight UT
9136.544 sec
~ 152.28 min
~ 2.54 hr
Timestamp

## Slide 35: IPv4 Header

## Slide 36: Header Fields (1)
Version
  Currently 4
  IP v6 - see later
Internet header length
  In 32 bit words
  Including options
Type of service (DS/ECN)
Total length
  Of datagram, in octets
DS: Differentiated Service
ECN: Explicit Congestion Notification

## Slide 37
DS/ECN

## Slide 38: Header Fields (2)
Identification
  Sequence number
  Used with addresses and user protocol to identify datagram uniquely
Flags
  More bit
  Don’t fragment
Fragmentation offset
Time to live
Protocol
  Next higher layer to receive data field at destination
0
DF
MF

## Slide 39: Protocol
Protocol: 8 bits
  Identifies contents of data field
  1 = ICMP
  6 = TCP
  17 =UDP
http://www.iana.org/assignments/protocol-numbers
IP
Header
Data Field
ICMP, TCP, or UDP Message

## Slide 40: Header Fields (3)
Header checksum
  Re-verified and recomputed at each router
  16 bit ones complement sum of all 16 bit words in header
  Set to zero during calculation
Source address
Destination address
Options
Padding
  To fill to multiple of 32 bits long

## Slide 41: Traceroute
To provide a trace of the path the packet took to reach the destination.
Operates by first sending out a packet with a Time To Live (TTL) of 1. The first hop then sends back an ICMP error message indicating that the packet could not be forwarded because the TTL expired.
The packet is then resent with a TTL of 2, and the second hop returns the TTL expired. This process continues until the destination is reached.
Record the source of each ICMP TTL exceeded message
RFC 1393

## Slide 42: tracert
C:\>tracert –d 163.22.7.6
Tracing route to 163.22.7.6 over a maximum of 30 hops
1 2 ms 4 ms <1 ms 10.10.13.254
2 <1 ms <1 ms <1 ms 163.22.1.253
3 <1 ms <1 ms <1 ms 163.22.7.6
Trace complete.

## Slide 44
http://www.visualroute.com/
VisualRoute

## Slide 45: Data Field
Carries user data from next layer up
Integer multiple of 8 bits long (octet)
Max length of datagram (header plus data) 65,535 octets

## Slide 46: IPv4 Address Formats
0 ~ 127
128 ~ 191
192 ~ 223
224 ~ 239
240 ~

## Slide 47: IP Addresses - Class A
32 bit global internet address
Network part and host part
Class A
  Start with binary 0
  All 0 reserved (0.0.0.0)
  01111111 (127) reserved for loopback
  Range 1.x.x.x to 126.x.x.x
  All allocated
http://www.iana.org/assignments/ipv4-address-space

## Slide 48: IP Addresses - Class B
Start 10
Range 128.x.x.x to 191.x.x.x
Second Octet also included in network address
214 = 16,384 class B addresses
All allocated

## Slide 49: IP Addresses - Class C
Start 110
Range 192.x.x.x to 223.x.x.x
Second and third octet also part of network address
221 = 2,097,152 addresses
Nearly all allocated
  See IPv6

## Slide 50: Private IP Addresses
Any organization can use these inside their network
Can’t go on the internet. [RFC 1918]
  10.0.0.0 - 10.255.255.255 (10/8 prefix)
  172.16.0.0 - 172.31.255.255 (172.16/12 prefix)
  192.168.0.0 - 192.168.255.255 (192.168/16 prefix)
1
16
256

## Slide 51: Subnets and Subnet Masks
Allow arbitrary complexity of internetworked LANs within organization
Insulate overall internet from growth of network numbers and routing complexity
Site looks to rest of internet like single network
Each LAN assigned subnet number
Host portion of address partitioned into subnet number and host number
Local routers route within subnetted network
Subnet mask indicates which bits are subnet number and which are host number

## Slide 53: Special IP Addresses
All-0 host suffix Þ Network Address
  163.22.20.16/24  163.22.20.0/24
  163.22.20.137/26  163.22.20.?/26
    163.22.20.137: 163.22.20.10001001  163.22.20.10000000 (163.22.20.128/26)
All-0s Þ This computer
  0.0.0.0
All-0s network Þ This network.
  163.22.20.7/24  0.0.0.7 (Host 7 on this network)
All-1 host suffix Þ All hosts on the destination net
  (directed broadcast)
    163.22.20.16/24  163.22.20.255
All-1s Þ All hosts on this net (limited broadcast)
  255.255.255.255
  Subnet number cannot be all 1
127.*.*.* Þ Loopback through IP layer
  127.0.0.1

## Slide 54: Question
一個原為Class C之IP網路，均分成多個子網路遮罩為255.255.255.224的子網路後，將減少____ 個可配置的主機位址。(96研)
Hints:
  Class C: 255.255.255.0
  224: 11100000
  host all 0’s: Network ID
  host all 1’s: Broadcast address

## Slide 55
Host: 10.10.4.26
Subnet mask: 255.255.255.0
Default Gateway: 10.10.4.254
Send a packet destined to 10.10.4.35
  10.10.4.35 AND 255.255.255.0 ?= 10.10.4.26 AND 255.255.255.0  Yes, the same subnet
  Send to 10.10.4.35 directly
Send a packet destined to 10.10.6.3
  10.10.6.3 AND 255.255.255.0 ?= 10.10.4.26 AND 255.255.255.0  No, the different subnets
  Send to default gateway (10.10.4.254)

## Slide 56: Routing Table
For each row [i]:
if ((Mask[i] & Destination Addr) = = Destination[i])  Match!
if row[i] is the best match
forward to NextHop[i]

## Slide 57
C:\>route print
===========================================================================
Interface List
0x1 ........................... MS TCP Loopback interface
0x10003 ...00 15 f2 ec 4a 50 ...... Intel(R) PRO/1000 PL Network Connection
===========================================================================
===========================================================================
Active Routes:
Network Destination Netmask Gateway Interface Metric
0.0.0.0 0.0.0.0 10.10.13.254 10.10.13.137 20
10.10.13.0 255.255.255.0 10.10.13.137 10.10.13.137 20
10.10.13.137 255.255.255.255 127.0.0.1 127.0.0.1 20
10.255.255.255 255.255.255.255 10.10.13.137 10.10.13.137 20
127.0.0.0 255.0.0.0 127.0.0.1 127.0.0.1 1
224.0.0.0 240.0.0.0 10.10.13.137 10.10.13.137 20
255.255.255.255 255.255.255.255 10.10.13.137 10.10.13.137 1
Default Gateway: 10.10.13.254
===========================================================================
Persistent Routes:
None
C:\>
C:\> route print

## Slide 58: Routing Table
Row
Destination
Network or
Subnet
Mask (/Prefix)*
Metric
(Cost)
Next-
Hop
Router
Interface
1
128.171.0.0
255.255.0.0 (/16)
47
G
2
2
172.30.33.0
255.255.255.0 (/24)
0
Local
1
3
192.168.6.0
255.255.255.0 (/24)
12
G
2
Routers Base Routing Decisions on Their Routing Tables.
Each Row Represents a Route to a Network or Subnet
For Each Arriving Packet, The Packet’s Destination IP Address Is Matched Against the Destination Network or Subnet Field in Every Row

## Slide 59: Routing Table
Row
Destination
Network or
Subnet
Mask (/Prefix)*
Metric
(Cost)
Next-
Hop
Router
Interface
1
128.171.0.0
255.255.0.0 (/16)
47
G
2
2
172.30.33.0
255.255.255.0 (/24)
0
Local
1
3
192.168.6.0
255.255.255.0 (/24)
12
G
2
Each Row Represents a Route to a Network or Subnet.
All packets to that network or subnet are governed by that one row.
So there is one rule for a range of IP addresses. This reduces the number of rows that must be considered.

## Slide 60: Routing Table
Row 1
If Destination IP Address = 172. 30.33.6
Mask = 255.255. 0.0
Result = 172. 30. 0.0
Destination Network or Subnet = 128.171. 0.0
No match!
Row
Destination
Network or
Subnet
Mask (/Prefix)*
Metric
(Cost)
Next-
Hop
Router
Interface
1
128.171.0.0
255.255.0.0 (/16)
47
G
2
2
172.30.33.0
255.255.255.0 (/24)
0
Local
1
3
192.168.6.0
255.255.255.0 (/24)
12
G
2

## Slide 61: Routing Table
Row
Destination
Network or
Subnet
Mask (/Prefix)*
Metric
(Cost)
Next-
Hop
Router
Interface
1
128.171.0.0
255.255.0.0 (/16)
47
G
2
2
172.30.33.0
255.255.255.0 (/24)
0
Local
1
3
192.168.6.0
255.255.255.0 (/24)
12
G
2
Row 1
If Destination IP Address = 172. 30. 33.6
Mask = 255.255.255.0
Result = 172. 30. 33.0
Destination Network or Subnet = 172. 30. 33.0
This row is a match!

## Slide 62: Routing Table
Row
Destination
Network or
Subnet
Mask (/Prefix)*
Metric
(Cost)
Next-
Hop
Router
Interface
1
128.171.0.0
255.255.0.0 (/16)
47
G
2
2
172.30.33.0
255.255.255.0 (/24)
0
Local
1
3
192.168.6.0
255.255.255.0 (/24)
12
G
2
Row 3
If Destination IP Address = 172. 30. 33.6
Mask =
Result =
Destination Network or Subnet =
Is this row is a match?

## Slide 63: Routing
For Each Incoming IP Packet
  Destination IP address is matched against every row in the routing table.
  If the routing table has 10,000 rows, 10,000 comparisons will be made for each packet.
  There can be multiple matching rows for a destination IP address, corresponding to multiple alternative routes.
  After all matches are found, the best match must be selected.

## Slide 64: only one row matches
If only one row matches, it will be selected as the best row match.
  Destination IP address = 192.168.6.7
Row
Destination
Network or
Subnet
Mask (/Prefix)*
Metric
(Cost)
Next-
Hop
Router
Interface
3
192.168.0.0
255.255.0.0 (/16)
12
G
2

## Slide 65: Default Route
The default row always matches
  Mask 0.0.0.0 applied to anything results in 0.0.0.0.
  This always matches the Network/Subnet value 0.0.0.0.
  The router specified for this row (H) is the default router.
Row
Destination
Network or
Subnet
Mask (/Prefix)*
Metric
(Cost)
Next-
Hop
Router
Interface
15
0.0.0.0
0.0.0.0 (/0)
5
H
3

## Slide 66: Multiple Matches - 1
If there are multiple matches, the row with the longest length of match is selected
  This is Row 7 for 128.171.17.56 (24 bit match)
  Row 1’s length of match is only 16 bits
  Longer matches often are routes to a particular subnet within a network
Row
Destination
Network or
Subnet
Mask (/Prefix)*
Metric
(Cost)
Next-
Hop
Router
Interface
1
128.171.0.0
255.255.0.0 (/16)
47
G
2
7
127.171.17.0
255.255.255.0 (/24)
55
H
3

## Slide 67: Multiple Matches - 2
If there are multiple rows with the same lengths of match, the metric column compares alternative routes.
  If the metric is cost, the smallest metric wins (20)
  If the metric is speed, the largest metric wins (34)
Row
Destination
Network or
Subnet
Mask (/Prefix)*
Metric
(Cost)
Next-
Hop
Router
Interface
5
172.29.8.0
255.255.255.0 (/24)
34
F
1
8
172.29.8.0
255.255.255.0 (/24)
20
H
3

## Slide 68: IPv6 - Version Number
IP v 1-3 defined and replaced
IP v4 - current version
IP v5 - streams protocol
  Connection oriented internet layer protocol
IP v6 - replacement for IP v4
  During development it was called IPng
    Next Generation

## Slide 69: Why Change IP?
Address space exhaustion
  Two level addressing (network and host) wastes space
  Network addresses used even if not connected to Internet
  Growth of networks and the Internet
  Extended use of TCP/IP
  Single address per host
Requirements for new types of service

## Slide 70: IPv6 RFCs
1752 - Recommendations for the IP Next Generation Protocol
8200 - Overall specification
4291 - addressing structure
others (find them)
www.rfc-editor.org

## Slide 71: IPv6 Enhancements (1)
Expanded address space
  128 bit
Improved option mechanism
  Separate optional headers between IPv6 header and transport layer header
  Most are not examined by intermediate routes
    Improved speed and simplified router processing
    Easier to extend options
Address autoconfiguration
  Dynamic assignment of addresses

## Slide 72: IPv6 Enhancements (2)
Increased addressing flexibility
  Anycast - delivered to one of a set of nodes
  Improved scalability of multicast addresses (scope)
Support for resource allocation
  Replaces type of service
  Labeling of packets to particular traffic flow
  Allows special handling
  e.g. real time video

## Slide 73: IPv6 Structure
IPv6 header | Extension Header |    | Extension Header | Transport-level PDU
40 octets
0 or more
Hop-by-Hop Options
  Require processing at each router
Routing
  Similar to v4 source routing
Fragment
Authentication
Encapsulating security payload
Destination options
  For destination node
Extension Headers:

## Slide 74: IPv6 Extension Headers
IPv6 Header
Next Header=
Routing
TCP Header
Routing Header
Next Header=
TCP
IPv6 Header
Next Header=
Routing
TCP Header
Routing Header
Next Header=
Fragment
Fragment Header
Next Header=
TCP
IPv6 Header
Next Header=
TCP
Data
TCP Header
Data
Data
Without Extension Headers
With Extension Headers

## Slide 75: IPv6 Packet with Extension Headers
Next header

## Slide 76: IPv6 Header
Traffic Class

## Slide 77: IPv6 Header Fields (1)
Version
  6
Traffic Class (DS/ECN)
  Classes or priorities of packet
  Still under development
  See RFC 2460
Flow Label
  Used by hosts requesting special handling
Payload length
  Includes all extension headers plus user data

## Slide 78: IPv6 Header Fields (2)
Next Header
  Identifies type of header
    Extension or next layer up
  http://www.iana.org/assignments/protocol-numbers
Source Address
Destination address
0 = Hop-by-Hop Options
41 = ipv6
43 = Routing
44 = Fragment
51 = Authentication
60 = Destination Options
50 = Encapsulating Security Payload
58 = Internet Control Message Protocol (ICMP for IPv6)
59 = no next header

## Slide 79: Flow Label
Flow
  Sequence of packets from particular source to particular (unicast or multicast) destination
  Source desires special handling by routers
  Uniquely identified by source address, destination address, and 20-bit flow label
Router's view
  Sequence of packets sharing attributes affecting how packets handled
    Path, resource allocation, discard needs, accounting, security
  Handling must be declared
    Negotiate handling ahead of time using control protocol
    At transmission time using extension headers
      E.g. Hop-by-Hop Options header

## Slide 80: Flow Label Rules
Flow Label set to zero if not supported by host or router when originating
  Pass unchanged when forwarding
  Ignore when receiving
Packets from given source with same nonzero Flow Label must have same Destination Address, Source Address, Hop-by-Hop Options header contents (if present), and Routing header contents (if present)
  Router can make decisions by looking up flow label in table
Source assigns flow label
  New flow labels be chosen (pseudo-) randomly and uniformly
  Range 1 to 220 – 1
  Not reuse label within lifetime of existing flow
  Zero flow label indicates no flow label

## Slide 81: IPv6 Addresses
128 bits long
Assigned to interface
Single interface may have multiple unicast addresses
Three types of address
  unicast, anycast, multicast

## Slide 82: Types of address
Unicast
  Single interface
Anycast
  Set of interfaces (typically different nodes)
  Delivered to any one interface
  the “nearest”
Multicast
  Set of interfaces
  Delivered to all interfaces identified

## Slide 83: Text Representation of IPv6 Addresses
x:x:x:x:x:x:x:x
hexadecimal values of the eight 16-bit pieces of the address.
  FEDC:BA98:7654:3210:FEDC:BA98:7654:3210
  1080:0:0:0:8:800:200C:417A
It is not necessary to write the leading zeros in an individual field.
  0008  8, 0800  800
RFC 3513* / 4291
* RFC 3513 has been obsoleted by RFC 4291.

## Slide 84: IPv6 Address Representation (2)
The use of "::" indicates multiple groups of 16-bits of zeros.
Unicast address
  1080:0:0:0:8:800:200C:417A
  1080::8:800:200C:417A
Multicast address
  FF01:0:0:0:0:0:0:101  FF01::101
Loopback address
  0:0:0:0:0:0:0:1  ::1
unspecified addresses (Absence of address)
  0:0:0:0:0:0:0:0  ::

## Slide 85: IPv6 Address Representation (3)
IPv4 and IPv6 mixed address
  x:x:x:x:x:x:d.d.d.d
  x: IPv6, d: IPv4
  Eg.
    0:0:0:0:0:FFFF:129.144.52.38
    ::13.1.68.3
    ::FFFF:129.144.52.38

## Slide 86: Address Type Identification
Address type Binary prefix IPv6 notation
Unspecified 00...0 (128 bits) ::/128
Loopback 00...1 (128 bits) ::1/128
Global Unicast 001 2000::/3
Unique Local Unicast 1111 110 FC00::/7
Link Local Unicast 1111 1110 10 FE80::/10
Site-local unicast* 1111 1110 11 FEC0::/10
Multicast 1111 1111 FF00::/8
* No longer supported in new implementations
http://www.iana.org/assignments/ipv6-address-space/ipv6-address-space.xml

## Slide 87: Unicast Addresses
Global Unicast address
Unique Local Unicast address (RFC 4193)
  globally unique for local communications, usually inside of a site.
  Not expected to be routable on the global Internet.
  Routable inside of a limited area such as a site.
Link Local address (RFC 4291)
  for addressing on a single link for purposes such as automatic address configuration, neighbor discovery, or when no routers are present.
  Routers must not forward any packets with Link-Local source or destination addresses to other links.
Site-local address
  (Private IP addresses)

## Slide 88: IPv6 Global Unicast Address Assignments
https://www.iana.org/assignments/ipv6-unicast-address-assignments/ipv6-unicast-address-assignments.xhtml
Prefix | Designation | Date | WHOIS | RDAP | Status
2001:0000::/23 | IANA | 1999/7/1 | whois.iana.org |  | ALLOCATED
2001:0200::/23 | APNIC | 1999/7/1 | whois.apnic.net | https://rdap.apnic.net/ | ALLOCATED
2001:0400::/23 | ARIN | 1999/7/1 | whois.arin.net | https://rdap.arin.net/registry | ALLOCATED
 |  |  |  | http://rdap.arin.net/registry | 
2001:0600::/23 | RIPE NCC | 1999/7/1 | whois.ripe.net | https://rdap.db.ripe.net/ | ALLOCATED
2001:0800::/22 | RIPE NCC | 2002/11/2 | whois.ripe.net | https://rdap.db.ripe.net/ | ALLOCATED
2001:0c00::/23 | APNIC | 2002/5/2 | whois.apnic.net | https://rdap.apnic.net/ | ALLOCATED
2001:0e00::/23 | APNIC | 2003/1/1 | whois.apnic.net | https://rdap.apnic.net/ | ALLOCATED
2001:1200::/23 | LACNIC | 2002/11/1 | whois.lacnic.net | https://rdap.lacnic.net/rdap/ | ALLOCATED
2001:1400::/22 | RIPE NCC | 2003/7/1 | whois.ripe.net | https://rdap.db.ripe.net/ | ALLOCATED
2001:1800::/23 | ARIN | 2003/4/1 | whois.arin.net | https://rdap.arin.net/registry | ALLOCATED
 |  |  |  | http://rdap.arin.net/registry | 
2001:1a00::/23 | RIPE NCC | 2004/1/1 | whois.ripe.net | https://rdap.db.ripe.net/ | ALLOCATED
2001:1c00::/22 | RIPE NCC | 2004/5/4 | whois.ripe.net | https://rdap.db.ripe.net/ | ALLOCATED
2001:2000::/19 | RIPE NCC | 2019/3/12 | whois.ripe.net | https://rdap.db.ripe.net/ | ALLOCATED
2001:4000::/23 | RIPE NCC | 2004/6/11 | whois.ripe.net | https://rdap.db.ripe.net/ | ALLOCATED
2001:4200::/23 | AFRINIC | 2004/6/1 | whois.afrinic.net | https://rdap.afrinic.net/rdap/ | ALLOCATED
 |  |  |  | http://rdap.afrinic.net/rdap/ | 
2001:4400::/23 | APNIC | 2004/6/11 | whois.apnic.net | https://rdap.apnic.net/ | ALLOCATED

## Slide 89
A coordinating body for the world’s Regional Internet Registries (RIRs)
Number Resource Organization (NRO)

## Slide 90: IPv6 Unicast Addresses
node address
subnet prefix
interface ID
128 bits
n bits
128-n bits
n = 64  8+8

## Slide 91: Global Unicast Addresses
subnet ID
interface ID
n bits
128-n-m bits
global routing prefix
m bits
Site
Link

## Slide 92: Local-Use IPv6 Unicast Addresses
Link-Local Unicast Addresses
Site-Local Unicast Addresses
1111111010
0
Interface ID
10 bits
54 bits
64 bits
1111111011
0
Interface ID
10 bits
38 bits
64 bits
Subnet ID
16 bits
FE80::x:x:x:x
FEC0::s:x:x:x:x
fe80::98bc:4ce7:aae8:fed5

## Slide 93: Multicast Addresses
11111111
Group ID
8 bits
4 bits
112 bits
Flags
Scope
4 bits
0000 : well known
0001 : transient
0 reserved
1 Interface-Local scope
2 Link-Local scope
3 reserved
4 Admin-Local scope
5 Site-Local scope
6 (unassigned)
7 (unassigned)
8 Organization-Local scope
9 (unassigned)
A (unassigned)
B (unassigned)
C (unassigned)
D (unassigned)
E Global scope
F reserved
Flags:
Scope:
(loopback)
(multiple sites)

## Slide 94: IPv6 Extension Headers
http://www.iana.org/assignments/ipv6-parameters

## Slide 95: Hop-by-Hop Options
Next header
Header extension length
Options
  Pad1
    Insert one byte of padding into Options area of header
  PadN
    Insert N (2) bytes of padding into Options area of header
    Ensure header is multiple of 8 bytes
  Jumbo payload
    Over 216 = 65,535 octets
  Router alert
    Tells router that contents of packet is of interest to router
    Provides support for RSPV

## Slide 96: Fragmentation Header
Fragmentation only allowed at source
No fragmentation at intermediate routers
Node must perform path discovery to find smallest MTU of intermediate networks
Source fragments to match MTU
Otherwise limit to 1280 octets
RFC 1981: Path MTU Discovery for IP version 6

## Slide 97: Fragmentation Header Fields
Next Header
Reserved
Fragmentation offset
Reserved
More flag
Identification

## Slide 98: Routing Header
List of one or more intermediate nodes to be visited
Next Header
Header extension length
Routing type
Segments left
  i.e. number of nodes still to be visited

## Slide 99: Destination Options
Same format as Hop-by-Hop options header