## Slide 1: Carrier Wide Area Networks (WANs)
Chapter 10
Panko and Panko
Business Data Networks and Security, 10th Edition, Global Edition
Copyright © 2015 Pearson Education, Ltd.

## Slide 2
Corporate WANs
Network Access
The Network Core
WAN Optimization
More on SDN

## Slide 3: 10.1: LANs versus WANs (and MANs)
Category | Local Area Network | Metropolitan Area Network | Wide Area Network
Abbreviation | LAN | MAN | WAN
Service Area | On customer premises (home, office, apartment, building, campus, etc.) | Between sites in a metropolitan area. (city and its suburbs) A Type of WAN | Between sites in a region, a country, or around the world.

## Slide 4: 10.1: LANs versus WANs (and MANs)
Category | Local Area Network | Metropolitan Area Network | Wide Area Network
Implementation | Self | Carrier | Carrier
Ability to Choose Technology | High | Low | Low
Who Manages the Network? | Self | Carrier | Carrier

## Slide 5: 10.1: LANs versus WANs (and MANs)
Category | Local Area Network | Metropolitan Area Network | Wide Area Network
Price | Highly related to cost | Based on pricing strategy. Highly unpredictable. | Based on pricing strategy. Highly unpredictable.
Cost per Bit Transmitted | Low | Medium | High
Typical Transmission Speed |  1 Gbps | 10 Mbps ~ 1 Gbps | 1 ~ 100 Mbps

## Slide 6: 10.1: LANs versus WANs (and MANs)
Category | Local Area Network | Metropolitan Area Network | Wide Area Network
Diversity of Technologies | Low: 802.3 and 802.11 | Medium | High

## Slide 7: Corporate WANs
The Internet
  Ubiquitous and inexpensive
  Lacks the QoS requirements of organizations
Corporate WANs
  Offer the required QoS
  Much more expensive than the Internet to meet traffic engineering requirements
  Mostly for transmission between a corporation’s sites

## Slide 8
Corporate WANs
Network Access
The Network Core
WAN Optimization
More on SDN

## Slide 9: 10.3: Basic WAN Components
Copyright © 2015 Pearson Education, Ltd.
(CPE)
(Access Link)
(CPE)

## Slide 10: 10.4: The Public Switched Telephone Network (PSTN)
See Page 370
https://en.wikipedia.org/wiki/PSTN_network_topology

## Slide 11: 10.4: The Public Switched Telephone Network (PSTN)

## Slide 12: 10.5: Asymmetric Digital Subscriber Line (ADSL)
The local loop brings a 1-pair voice grade UTP line to every household
Not designed to carry data
ADSL uses advanced technology to deliver data over these 1-pair VG lines
The lines are already installed, so there is no need to run a new line to the subscriber
This makes ADSL inexpensive

## Slide 13: 10.5: Asymmetric Digital Subscriber Line (DSL) Service for Residences

## Slide 14: 10.5: Asymmetric Digital Subscriber Line (DSL) Service for Residences

## Slide 15: 10.5: Asymmetric Digital Subscriber Line (DSL) Service for Residences
DSLAM = DSL Access Multiplexer

## Slide 16: Cable Modem Service
Coaxial cable service was created to bring television to homes that had poor over-the- air reception
Now also offers two-way data service called cable modem service
Popular in the United States
Not popular in most countries

## Slide 17: 10.7: Coaxial Cable
Two conductors: central wire and coaxial ring

## Slide 18: 10.6: Cable Modem Service
1
8
7
6
5
4
3
2

## Slide 19: 10.6: Cable Modem Service

## Slide 20: ADSL versus Cable Modem Service
In general …
Cable modem service offers somewhat faster individual throughput at a somewhat higher cost.
ADSL service offers somewhat slower individual throughput at a somewhat lower cost.

## Slide 21
2. Cell
3. Cellsite
4. Channel Reuse
5. Handoff
Cellular Telephone Service

## Slide 22: 10.8: Cellular Telephone Service
Note that a cell is a geographical region while a cellsite is a building with cellular equipment

## Slide 23: 10.8: Cellular Telephone Service
4.
A channel can be reused in multiple cells.
The carrier can serve more customers.

## Slide 24: Cellular Technology
Channel Reuse
  The same channel can be used in multiple cells.
    This allows subscribers in different sites to use the same channel.
    Consequently, the carrier can serve multiple customers per channel.
    This is the reason for using cells
    (Having multiple access points in an 802.11 Building WLAN serves the same purpose)

## Slide 25: Cellular Technology
Channel Reuse
  Example without channel reuse:
    If 500 channels, only 500 simultaneous subscribers can be served in the entire system.
  Example with channel reuse in each cell
    500 channels
    100 cells
    Can serve 50,000 simultaneous subscribers

## Slide 26: 10.8: Cellular Technology
If you travel between cells, you will be handed off to a new cell site in the new cell (P)
5. Handoff

## Slide 27: 10.8: Cellular Telephony
Placing a call from a mobile phone to a wireline customer.
(Or vice versa)

## Slide 28: 10.9: Cellsite for Mobile Telephones
Cellsite
Cellular
Antennas
Point-to-Point Microwave
Antenna to MTSO

## Slide 29: 10.10: Cellular Data Speeds
Speeds
  Early cellular systems were limited to about 20 kbps
  Today, most carriers give peak download speeds of 5 to 10 Mbps with the best giving 15 to 20 Mbps
  100 Mbps is on the horizon
  Nearly all carriers now use LTE (long-term evolution) technology

## Slide 30: 10.10: Cellular Data Speeds
LTE Advanced
  The next generation of LTE
  Currently, speeds are required to be 3 Gbps downstream, half of that upstream
3G, 4G, and 5G
  The ITU creates definitions of generations
  Marketers are using the terms in a meaningless manner

## Slide 31: 10.10: Cellular Data Speeds
Throughput Differs Widely from Rated Speeds
  There is extensive overhead in cellular transmission. The data transmission rate is always less than the bit transmission rate.
  If the user is riding in a car, throughput will fall.
  If more customers use a cellsite, the cellsite may have to decrease the transmission speed to each.
  In particular, speed will depend on the time of day.
Copyright © 2015 Pearson Education, Ltd.

## Slide 32: 10.10: Cellular Data Speeds
Throughput Differs Widely from Rated Speeds
  If the user travels into an area with an overloaded cellsite, speed will be lower.
  At greater distances from a cellsite, speed falls, just as in Wi-Fi.
  Weakened signal strength caused by transmission through buildings will also reduce speed.
Copyright © 2015 Pearson Education, Ltd.

## Slide 33
Corporate WANs
Network Access
The Network Core
WAN Optimization
More on SDN

## Slide 34: 10.3: Basic WAN Components and Business Uses
Copyright © 2015 Pearson Education, Ltd.
(CPE)
(CPE)
(Access Link)

## Slide 35: 10.11: Wired Carrier WANs for Business
Corporations need to connect their sites with high-quality transmission networks with better QoS than the Internet

## Slide 36: Wired Carrier WAN Core Technologies
Leased Lines
  Layer 1
  Access lines
  Leased line networks
Carrier Ethernet
  Layer 2
  Extends site Ethernet LANs to the corporation
Multiprotocol Label Switching (MPLS)
  Layer 3
  Strong traffic engineering for high QoS
https://www.cht.com.tw/home/enterprise

## Slide 37: 10.11: Wired Carrier WANs for Business
A
F
E
D
C
B
專線
A lease line is also used from a company to the ISP's nearest location, called a point of presence (POP).

## Slide 38: 10.12: Access Lines vs Leased Lines
Each customer site must have a CSU/DSU interface to the telephone network.
CSU/DSU :
Channel Service Unit / Data Service Unit
Trunk
Line
Trunk
Line

## Slide 39: 10.13: Leased Line Data Network

## Slide 40: 10.13: Leased Line Data Network

## Slide 41: 10.14: Leased Line Speeds
North American Digital Hierarchy |  | 
Line | Speed | Typical Transmission Medium
T1* | 1.544 Mbps | 2-Pair Data-Grade UTP
T3 | 44.736 Mbps | Carrier Optical Fiber

## Slide 42: 10.14: Leased Line Speeds
CEPT Hierarchy (Europe) |  | 
Line | Speed | Typical Transmission Medium
E1* | 2.048 Mbps | 2-Pair Data-Grade UTP
E3 | 34.368 Mbps | Carrier Optical Fiber

## Slide 43: 10.14: Leased Line Speeds
T1*, E1*
Often offer synchronous DSL over existing 1-pair VG UTP rather than offering traditional T1 and E1 service over 2-pair data grade UTP, which must be pulled to the customer’s premises.

## Slide 44: 10.14: Leased Line Speeds
Fractional T1 speeds are often offered by carriers. These typically include some subset of the speeds 128 kbps, 256 kbps, 384 kbps, 512 kbps, and 768 kbps.
T1 and E1 lines can be bonded to provide double, triple, or quadruple the capacity of a single line

## Slide 45: 10.14: Leased Line Speeds
SONET/SDH Speeds |  | 
Line | Speed (Mbps) | Transmission Medium
OC3/STM1 | 155.52 | Carrier Optical Fiber
OC12/STM4 | 622.08 | Carrier Optical Fiber
OC48/STM16 | 2,488.32 | Carrier Optical Fiber
OC192/STM64 | 9,953.28 | Carrier Optical Fiber
OC768/STM256 | 39,813.12 | Carrier Optical Fiber
Above 50 Mbps, transmission lines are standardized

## Slide 46
https://www.cht.com.tw/home/enterprise/hinet/hinet-line/domestic-circuit
中華電信
長途數據電路
月租費

## Slide 47: 10.15: Public Switched Data Network (PSDN)

## Slide 48: 10.15: Public Switched Data Network (PSDN)
Switched (Layer 2) Technology
  Carrier Ethernet
    Yes, Ethernet
  Historical PSDN technologies
    Dead or dying
    Frame Relay
    ATM (Asynchronous Transfer Mode)

## Slide 49: 10.16: Carrier Ethernet PSDN Services
E-Line service is like having a leased line

## Slide 50: 10.16: Carrier Ethernet PSDN Services
E-LAN service extends site Ethernet LANs to cover multiple sites

## Slide 51: 10.17: Carrier Ethernet Attractions
Low cost
Familiarity of the technology for the firm’s networking staff
High speeds are available
Speed agility: Increases in speed can be provisioned rapidly
Quality of service
Security

## Slide 52: Multiprotocol Label Switching
Routers route each packet individually, going through the three steps we saw in the last chapter.
  Even if the next packet is going to the same destination IP address, the router will go through all three steps.
  This consumes a great deal of processing power per packet.
  This makes traditional routing expensive.

## Slide 53: Multiprotocol Label Switching
MPLS addresses this issue.
  Routers identify the best route for a range of IP addresses before sending data.
  That route is given a label number.
  Each packet in a stream gets a label with this label number.
  Routers do only a quick table lookup per packet.
  Table lookups require little processing power.
  So multiprotocol label switching is much less expensive than traditional routing.

## Slide 54: 10.18: Multiprotocol Label Switching (MPLS)

## Slide 55: 10.18: Multiprotocol Label Switching (MPLS)
Label Number is 123

## Slide 56: 10.18: MPLS
Label sits between the frame header and the IP packet header.
IP Packet
Header
MPLS Label
Frame Header

## Slide 57: 10.18: Multiprotocol Label Switching (MPLS)
Router 3 sends the packet out through Interface 1

## Slide 58: 10.18: Multiprotocol Label Switching (MPLS)

## Slide 59: 10.18: Multiprotocol Label Switching (MPLS)